## Slide 1: Silicon Smart by Synopsys
Presentation by: Oshin Jakhete

## Slide 2: INTRODUCTION
SiliconSmart is a Synopsys tool which allows the user to characterize the timing, power, and function for a standard cell or macro for use with other Synopsys tools.
SiliconSmart uses spice-level simulation (be it HSPICE, FineSIM, etc.) to characterize a cells timing and power characteristics, and to ensure that the cell functions as specified.

## Slide 3: Goal
Process of importing a netlist directory, editing instance files, configuring and characterizing standard cells, and writing a liberty file with the timing and power information for each cell.
Inputs Required:
Netlist file
Model Library
Outputs Produced:
.inst file
.lib file

## Slide 4: .tcl file
We need to edit the configure.tcl file under my_library/config.
We need to set the accurate device model files as well as specify the simulation used (in our case SPICE simulation)

## Slide 5: Characterization and Final results.
After running all the necessary scripts, we model the cells.
After modelling the cells, the software generates a .lib file which contains all the timing and power characteristics.
This .lib file is the desired output which can be used in other synopsys tools like library compiler.

## Slide 6: Methodology
Create a folder which will contain the .tcl file and all the other results and files after running the scripts.
Edit the .tcl file to set the models and the simulator.
Import the netlists which are in the .spice format.
Configure the one or more cells by using the "configure" command.
Characterize the timing and power characteristics of the cells by using the "characterize" command.
To get the desired liberty file use the command "model". This will generate the output .lib file which can be used in the other Synopsys tools.

## Slide 7: Thank You